## Slide 1
DCT1
DC Energy Meter
Launch Presentation
September 2023

## Slide 2
Contents
INTRODUCTION
Why this launch ?
Expectations
Typical applications
THE PRODUCT
Part numbers
Relevant technical data
THE MARKET
Main competitors
Battlecard
Relevant applications
Marketing tools
Certifications

## Slide 3
Introduction
Why this launch?
To provide a reliable and accurate metering system for fast, ultra-fast, hyper-fast chargers, in order to avoid the anachronistic charge-by-time method, or inaccurate results using upstream AC metering system.
DCT1 is the first answer of Carlo Gavazzi to this need. A very flexible, simple, compact, and easy-to-integrate solution for energy metering in fast chargers.
With DCT1 we can provide a metering system that can be certified within the US and German calibration law requirements and that can be applied for the legal use in different European Countries, while waiting for a harmonized and common European Union regulation.
Furthermore, DCT1 can be used for accurate measurements (according to the most recent IEC standard for DC energy) in other emergent applications using DC current:
    DC industry
    PV Energy Storage for big industries/commercial building
    DC Microgrids

## Slide 4
Introduction
Expectations
  Consolidate our presence in the e-mobility market being able to offer a comprehensive range of AC and DC meters
  Expand our existing DC meter offering which presently includes CPA and VMUE, offering enhanced accuracy, voltage range and communication not available in other families
  Enter the market while developing new features (in particular a new version equipped with a remote display) to meet future DC metering requirements and standards (MID extension to DC)
  Acquire commercial and technical know-how as the base for future product development and business opportunities
  To satisfy customer needs, both current and emerging, thanks to the experience gained with AC products for EV chargers and with the cooperation of key partners in the e-mobility working group

## Slide 5
Introduction
Typical applications
EV charging stations
PV energy storage
DC industry

## Slide 6
The product
Relevant technical data
Class 1 (kWh) according to EN62053-41 or class A according to VDE-AR-E 2418-3-100 Annex A
Accuracy: ±0.5% RDG (current/voltage)
Voltage inputs: 150 to 1000 V dc
Auxiliary power supply 12 or 24 V dc
Current inputs: direct connection up to 600 A (DCT1A60) or up to 300 A (DCT1A30)
Real time variables: V, A, W
Energy measurements (total imported and exported, partial imported and exported): kWh
Energy resolution 0.0001 kWh (0.1 Wh)
Ampere-hour meters (total imported and exported, partial imported and exported): Ah
Run hour meters (relevant to both imported/exported energy, total and partial)
Total operating time (total/partial)
RS485 Modbus RTU (S1 without signature, S2 with 256 bit signature, S3 with 384 bit signature) or SML (384 bit signature)
Communication data refresh time: 200 ms
cULus approval
NMi evaluation certificate for Eichrecht approval according to IEC 62052-11, IEC 62052-31, IEC 62053-41, VDE-AR-E 2418-3-100 Annex A, WELMEC 7.2
DIN-rail or back panel (via screw terminals) mounting
Horizontal or vertical mounting

## Slide 7
The product
Part numbers
Part number | Voltage input | Current input | Port | Certifications
DCT1A60V10LS1X | 150 to 1000 V | 6-120 (600) A | RS485 Modbus RTU | CE, UKCA, cULus
DCT1A60V10LS2EC | 150 to 1000 V | 6-120 (600) A | RS485 Modbus RTU, 256 bit signature | CE, UKCA, cULus + evaluation certificate*
DCT1A60V10LS3EC | 150 to 1000 V | 6-120 (600) A | RS485 Modbus RTU, 384 bit signature | CE, UKCA, cULus + evaluation certificate*
DCT1A60V10LK1EC | 150 to 1000 V | 6-120 (600) A | SML, 384 bit signature | CE, UKCA, cULus + evaluation certificate*
DCT1A30V10LS1X | 150 to 1000 V | 2.5-50 (300) A | RS485 Modbus RTU | CE, UKCA, cULus
DCT1A30V10LS2EC | 150 to 1000 V | 2.5-50 (300) A | RS485 Modbus RTU, 256 bit signature | CE, UKCA, cULus + evaluation certificate*
DCT1A30V10LS3EC | 150 to 1000 V | 2.5-50 (300) A | RS485 Modbus RTU, 384 bit signature | CE, UKCA, cULus + evaluation certificate*
DCT1A30V10LK1EC | 150 to 1000 V | 2.5-50 (300) A | SML, 384 bit signature | CE, UKCA, cULus + evaluation certificate*
* evaluation certificate according to IEC 62052-11, IEC 62052-31, IEC 62053-41, VDE-AR-E 2418-3-100 Annex A, WELMEC 7.2

## Slide 8
The market
Refer to file named:
Cross_reference_DCT1.xlsx
Main competitors
Product name | Strength | Weakness | Prod. picture
DCT1 | Compact housing Cable loss compensation Bidirectional energy certificate Eichrecht compliance 384 bit signature | No display (till DCM1 is avaialble) | 
LEM DCBM | Cable loss compensation Display LNE, Eichrecht compliance | Only split concept | 
DZG GSH01 | Compact housing Display | No UL approval | 
Isabellenhutte IEM-DCC | Cable loss compensation Display Eichrecht compliance | Non bidirectional Huge size No UL approval | 
AST DC-METER | Cable loss compensation Display LNE, Eichrecht compliance Single device or split concept | Only high power versions Big size | 

## Slide 9
The market
Battlecard DCT1 – DC metering for fast chargers
Signed data transmission
256 bit or 384 bit signature to guarantee authenticity of transmitted data via Modbus RTU or SML
Cable loss management
Cable resistance parameter to calculate only energy provided to the battery, removing losses in the cable
Temperature monitoring
Real time shunt temperature monitoring via serial communication without additional sensors
Flexible connection
Compatibility with both busbars and cable lugs, vertical or horizontal connection
Target Industries & Applications
EV charging stations
  Fast chargers
PV energy storage
  Utility battery storage
Energy and building efficiency
  DC industry
  Microgrids
Key Benefits
Tamper-proof
Sealable measuring inputs and communication port for secure data transmission
Diagnostics
Warning over LEDs or serial communication in case of overtemperature, overcurrent or overvoltage
Fast refresh time
200 ms refresh time on serial communication
Competitor Products
Unique Value Proposition
LEM
DCBM
DZG
GSH01
Isabellenhutte
IEM-DCC
AST
DC-METER

## Slide 10
The market
Relevant applications – DC metering in electric vehicle fast chargers
Customer need Fast charger manufacturers for electric vehicles need a DC meter able to accurately measure the amount of energy provided to the battery and transmit data to the controller in a secure way, in order to correctly bill the customer. AC meters upstream from the AC/DC converter provide inaccurate measurement because they consider also losses given by the AC/DC conversion and the losses in the cable.
Our Solution
DCT1 is installed on the DC side and is compatible with most of the DC chargers on the market thanks to the wide voltage and current measuring range. Thanks to the cable loss compensation function, only energy provided to the vehicle battery is considered, removing the losses due to the cable resistance. Data transmitted to the controller are signed to guarantee data authenticity.
Benefits
Wide measuring range up to 1000 V, 300 or 600 A
Cable loss compensation
Signed data transmission (256 bit or 384 bit)

## Slide 11
The market
Marketing tools
Data Sheets
DCT1_DS
Available in:
Chinese, Danish, English, French, German, Italian, Spanish and Swedish

## Slide 12
The market
Certifications
Environmental Management System: ISO 14001:2015
Quality Management System: ISO 9001:2015
According to Low Voltage Directive 2014/35/EU According to EMC Directive 2014/30/EU
According to RoHS Directive 2011/65/EU & Delegated Directive 2015/863
North America: UL61010-1
Evaluation certificate for Eichrecht approval according to IEC 62052-11, IEC 62052-31, IEC 62053-41, VDE-AR-E 2418-3-100 Annex A, WELMEC 7.2